## Slide 1: A next generation in-situ radiometer
Arrow Lee, Tim Nightingale and Werenfrid Wimmer

## Slide 2: Outline
Background to next-generation radiometer study
Summary of requirements
Design features

## Slide 3: Introduction
CCN to current FRM4SST contract: “WP80: Case study for a next generation radiometer”
We’re tasked to:
  Consider the basis for a new generation of in situ radiometers,
  Concentrate on validation activities,
  Survey different measurement approaches, particularly infrared broadband and spectro-radiometry and microwave radiometry,
  Review experience with existing instruments,
  Propose an outline design for a new instrument.
We also want to give more attention to issues such as:
  Manufacturability
  Ease of optical alignment
  Maintainability
  Ease of deployment
  Electrical and mechanical interfaces

## Slide 4: The usual suspects
From left to right: SISTeR, ISAR, CIRIMS, M-AERI and DAR011 on the R/V F.G. Walton Smith in 2001

## Slide 5: Requirements
SST systematic uncertainty < 100 mK 1σ (50 mK goal)
  Includes retrieval, ancillary data, model uncertainties
  BT systematic uncertainty tighter
Clear traceability route for SST measurements
Autonomous operation
Straightforward use and maintenance

## Slide 6: Questions
Thermal infrared / microwave?
  Thermal infrared:
    Excellent calibration sources (internal and external)
    High sensitivity of basic sea radiance measurement to SST
    Well controlled beam pattern
    Close to ideal calibration scheme
  Microwave:
    Direct radiance measurements (including polarisation) in bands comparable to microwave satellite instruments, such as CIMR
    Correct skin depth for microwave intercomparisons

## Slide 7: Questions
Self-calibrating radiometer / nulling radiometer / other?
  Self-calibrating radiometer
    Robust, frequent end-to-end calibration of optical chain
    Possibility for self-traceability through on-board calibration targets
    Easily adapted for multiple viewing angles if equipped with scan mirror
  Nulling radiometer
    Black body compromises, as servo-ed to scene temperature
    Not ideal for sky measurements

## Slide 8: Questions
Imaging / non-imaging?
  Imaging
    Large exit aperture near to aperture plane (distant object plane)
    Fast sampling to avoid along-track smearing (poor noise performance)
    Small detector sizes to resolve image (poor noise performance)
    Likely to need cooled detectors for TIR
  Non-imaging
    Small exit aperture if placed at object plane (but divergent beam)
    Simple detector chain – chopping and synchronous detection possible
    Limited spatial resolution (tint * vship)
    Uncooled detector will give decent noise performance (30 mK @ 1 s)

## Slide 9: Questions
Single band / multiple bands / spectrometer?
  Single band
    Fine for SST but limited flexibility
  Multiple bands
    Increased complexity
    Possibilities to validate SST retrieval models
    Possibilities to retrieve other quantities (e.g. air temperature)
  Spectrometer
    Highest complexity
    Michelson / static FTS / grating / other?

## Slide 10: Questions
Which band(s)?
  3.7 µm
    High SST sensitivity (dB/dT) but few photons
  7.7 µm
    Lower atmospheric transmission, lower sensitivity to (distant) sky radiances
  10.8 µm
    Peak of Planck function
    Highest sea surface emissivity
  13 µm
    CO2 band for air temperature sounding?

## Slide 11: Questions
SST retrieval technique
  Sea + sky view
    A priori sea surface emissivity?
    Atmospheric line nulling?

## Slide 12: Questions
Other features?
  What would you like to see in a new instrument?